## Slide 1
Module 5:
Overall Equipment Effectiveness
Contents
Section 1: OEE Overview
Section 2: Shifts and Shift Schedules
Lab 8: Configuring Shift Schedules
Section 3: UCO and OCO Configuration for OEE Calculation
Lab 9: Tracking OEE
MES 2012 - Performance

## Slide 2: Overall Equipment Effectiveness
In Wonderware MES Performance, OEE calculation is based on the industry standard OEE methodology. The OEE calculation is a product of an entity’s Availability, Performance, and Quality efficiencies over a given interval (for example, a Shift)
OEE% = Availability% * Performance% * Quality%
  Availability% = Run Time / Net Operating Time
  Performance% = Total Output / Target Output
  Quality% = Good Output / Total Output

## Slide 3: OEE Calculation
Overall Equipment
Efficiency (OEE)
Availability
Performance
Quality
x
x
=
One Shift
Available Time
Not Scheduled (Lunch, Meeting)
Running Time
Down Time
Available Time – Down Time
Available Time
Availability% =
Actual Capacity
Speed Losses
Total Production _
Target Rate x Run Time
Performance% =
Total Production – Rejects
Total Production
Quality% =
Good Production
Bad Production
Target (Design) Capacity

## Slide 4
Shifts are user-defined names or labels used for OEE tracking
Shift Schedules define available time between a time period for OEE Availability calculation
Shift and Shift Schedule

## Slide 5: Lab 8 Configuring Shift Schedules
Lab Introduction
In this lab, you will:
Add “Production” entity to the Shift and Shift Schedule list
Create “Day” shift schedules
10 min

## Slide 6
A Work Order is needed
Batch Size cannot be zero
Target Job Production Rate is needed
Use .ProdAttrs.StartJobCmd and .ProdAttrs.EndJobCmd to start/stop a job
Use .ProdAttrs.ErrorCode and .ProdAttrs.ErrorMessage to monitor runtime error
UCO – Production Attributes

## Slide 7
Each Counter must be tied to a Production Reason
Each Counter has one absolute and one incremental counter attribute
Dead Band only applies to incremental counter
Use .CounterX.ErrorCode and .CounterX.ErrorMessage to monitor runtime error
OCO – Counters

## Slide 8: Lab 9 Tracking OEE
Lab Introduction
In this lab, you will:
Add and configure product counters in OCO template
Simulate product’s Good Count and Bad Count from an InTouch window
Track and verify OEE calculation
30 min