## Slide 1
Module 4:
Utilization
Contents
Section 1: Utilization Overview
Lab 4: Creating Utilization States and Reasons
Section 2: Utilization Capability Object Overview
Lab 5: Creating and Configuring Raw Reason Codes in the UCO
Lab 6: Adding Utilization States and Reasons
Section 3: Utilization Split
Lab 7: Splitting Utilizations
MES 2012 - Performance

## Slide 2: OEE Availability
One Shift
Available Time
Not Scheduled (Lunch, Meeting)
Running Time
Down Time
Available Time – Down Time
Available Time
Availability =

## Slide 3: OEE Time
Three prefixed conditions or labels that describe the effect of equipment Utilization State on OEE Availability
Positive effect on Availability
OEE Time
Runtime
Negative effect on Availability
Downtime
No effect on Availability
Neither

## Slide 4: Defining Utilization States
User-defined global list of equipment status, for equipment utilization records and availability calculation (by linking it to an OEE time)
  Contribute to OEE Runtime
    Running, Working, Open, On, etc.
  Contribute to OEE Downtime
    Down, Broken, Close, Off, etc.
  Contribute to OEE Neither
    Idle, Not Scheduled, etc.
Utilization States

## Slide 5: Defining Reasons
The various causes that keep the equipment in any particular State defined in Utilization States, for example, Down.
The list varies depending on:
  Individual production process
  Existing automation infrastructure
  Downtime Analysis requirements
  Project life-cycle
Reasons

## Slide 6: Defining Utilization
  Reason Name
  Utilization State
  OEE Time
Utilization

## Slide 7: Defining Utilization
Reason
Utilization State
OEE Time
Down
Idle
Running
Emergency Stop
Down
Runtime
Downtime
Neither
Downtime
The condition that caused
the equipment state change
User-Defined States and color
used to indicate the state of the
equipment when in this condition
How this condition affects the
Availability (Utilization) of the
Equipment

## Slide 8: Lab 4 Creating Utilization States and Reasons
Lab Introduction
In this lab, you will:
Create Utilization States
Create Utilizations (Reasons)
Use embedded MES Utilization Controls in an InTouch window to manually enter utilizations
15 min

## Slide 9
Production floor condition
Linked to an MES utilization reason
Priority based; only one reason at a time
Must have a default raw reason code
UCO – Raw Reason Code

## Slide 10: UCO – Raw Reason Code
Reason
Utilization State
OEE Time
Emergency Stop
Down
Downtime
E_Stop
Emergency Stop
Raw Reason Code
Default Reason
MyContainer.E_Stop
00:00:00.000
Minimum Time
Expression
Reason
Utilization State
OEE Time
Emergency Stop
Down
Downtime
GuardSw
Emergency Stop
MyContainer.GuardSw
00:00:00.000
Raw Reason Codes are UCO attributes used to connect to MES reasons
If required, multiple Raw Reason Codes can connect with the same MES reason.
MES Utilization
Raw Reason Code

## Slide 11
RRC evaluation – priority based
Default RRC always needed
RRC update frequency limit
Use .InAlarm for runtime alarm
Use .ErrorCode and .ErrorMessage for runtime error
UCO – Runtime Considerations

## Slide 12: Lab 5 Creating and Configuring RRCs in UCO
Lab Introduction
In this lab, you will:
Configure raw reason codes in a UCO template
Rebuild MES entity model
Simulate each raw reason code condition from InTouch
Monitor utilization updates in InTouch
Verify utilization reason counts in Pareto control and generate Downtime Analysis report from WIS
30 min

## Slide 13: Utilization States
Adding granularity to Utilization States
Utilization States
Down
Idle
Maintenance
Running
Running Slow
Down
Idle
Running
Down

## Slide 14: Lab 6 Adding Utilization States and Reasons
Lab Introduction
In this lab, you will:
Add a new utilization state
Add a reason sub group and new utilization reasons
Add new raw reason codes in UCO, including a prompt for user’s manual selection of reasons
30 min

## Slide 15
Utilization Split function enables user to:
Split an existing utilization into two or more segments
Modify the Start Time or End Time of an existing utilization
Change the reason for an existing utilization
Splitting Utilization

## Slide 16: Lab 7 Splitting Utilizations
Lab Introduction
In this lab, you will:
Split an existing utilization into two
Adjust the Start Time or End Time of the split utilization
Select a different reason for the split utilization
10 min