## Slide 1: 2
MES Client Configuration

## Slide 2: MES 2012 - Quality
Module 2:
MES Client Configuration
Contents
Section 1: MES Client
  Lab 1 – Setting Up and Enabling Security
Section 2: System Platform Configuration
  Lab 2 –Setting Up the Galaxy
Section 3: Further Preparation for MES Quality
  Lab 3 – Configuring the MES Client
Notes: This is the agenda for the Module.
It lists all the sections and labs for the module.

## Slide 3: MES Client
MES Client is the primary user interface for configuring MES Software functionality. As such there is some initial security configuration necessary prior to implementing any functionality.
  Security Policies
  Users and User Groups

## Slide 4: Lab 1 Setting up and Enabling Security
15 min

## Slide 5: Sample Recording Object
The Sample Recording Object (SRO) is an ArchestrA automation
object for two-way communication between the user and the
Wonderware MES database through the MES Middleware.
The SRO allows you to record data for one or more characteristics
and capture the following:
  Characteristic result data
  Contextual information related to a sample
  Contextual information related to a characteristic within a sample

## Slide 6: Sample Recording Object
The Sample Recording
Object, like other MES
objects, is imported from a
.aaPKG file that is part of
the MES installation.

## Slide 7: The Mixed Nuts Operation
Peanuts
Cashews
Almonds
Receiving
Roaster
Tank01
Tank02
Flavoring
Coater
Bagger
Boxer
Production
Quality implementation
  Roaster (SRO)
    Check for burnt nuts
  Bagger (SRO)
    Bag Weight
    Bag Quality
  Boxer (SRO)
    Box Weight
Warehouse
Shipping

## Slide 8: Lab 2 Setting Up the Galaxy
20 min

## Slide 9: Further Preparation for MES/Quality
Prior to MES/Quality implementation, additional general MES configuration may be necessary
  Entity Access for User Groups
    Users must have entity access to be able to configure entity functionality
  Entity Capabilities
    Defines which functions the entity can perform
  Units of Measure
    Provides a context for Quality data
  Shift definitions
    Used for data collection and reporting.

## Slide 10: Lab 3 Configuring the MES Client
10 min