## Slide 1: 3
MES Quality Configuration

## Slide 2: MES 2012 - Quality
Module 3:
MES Quality Configuration
Contents
Section 1: Sample Plan Configuration
  Lab 4 – Creating The Bag Weights Sample Plan
Section 2: The Sample Viewer Control
  Lab 5 – Working With The Sample Viewer Control
Section 3: Collecting Automatic Data
  Lab 6 – Configuring for Automatic Data Collection
Section 4: Additional Sample Plans
  Lab 7 – Creating The Nut Quality Sample Plan
  Lab 8 – Creating the Bag Quality Sample Plan
Section 5: Working With the Sample Recording Object
  Lab 9 – Exploring Additional Features of the SRO
Notes: This is the agenda for the Module.
It lists all the sections and labs for the module.

## Slide 3: Quality Management Configuration
Quality Management Configuration is composed of four elements
  Sample Plan Frequency
  Sample Plan
  Characteristic
  QM Specification

## Slide 4: Sample Plan Frequency
The Sample Plan Frequency definition determines the rate at which sample records will be generated
  Calendar Time
  Shift
  Job Start/End
  Lot Number Changes
  Manual (API)

## Slide 5: Sample Plan Frequency
Additional configuration can be done for
  Future Samples
    Represent upcoming samples
  Sample Warning / Expiry (optional)

## Slide 6: Sample Plan
The Sample Plan is responsible for
  Sample Naming Convention
    SamplePlanName Date Number (default)
    Numbering reset on date change
  Linking to the sample plan(s)

## Slide 7: Characteristic Definition
The Characteristic Definition establishes
  Unit of measurement
  Severity
  Default Chart
  Sample Details
    Decimal places
    Sample size
  Control Limit Source
    Calculation rules

## Slide 8: QM Specification
The QM (Quality Management) Specification Definition connects all the previous configuration details
  Sample Plan
  Characteristic

## Slide 9: QM Specification
  Adds additional configuration for
  Specification limits
  Data Entry limits
  Entity Connection
  Characteristic overrides
  Link to Rules

## Slide 10: Lab 4 Creating the Bag Weights Sample Plan
15 min

## Slide 11: Sample Viewer Control
  The Sample Viewer Control (SVC) is a .NET client control that allows
  the entry and editing of sample data and the generation of control
  charts

## Slide 12: Sample Viewer Control
  The SVC is built as an ArchestrA graphic in conjunction with the
  MES ButtonBar .NET control
  The Button Bar allows for
  Data Entry/Editing
  Sample Pulling
  Sample Finalization
  Data Filtering options
  Control Chart generation

## Slide 13: Sample Viewer Control
  Connection to the SVC will ask for initial filtering options including
  Sample Name
  Entity
  Sample Status
  Depending on configuration, you may also be prompted for entity Selection/Logon options

## Slide 14: Lab 5 Working with the Sample Viewer Control
25 min

## Slide 15: Automatic Data Acquisition
  Data acquisition options can be specified at the Sample Recording Object
  Characteristic link
  Delay Timer
    time between measurements
  Input Source

## Slide 16: Lab 6 Configuring for Automatic Data Collection
15 min

## Slide 17: Shift Based Sample Generation
  Shift based data collection allows for samples to be generated ONLY during defined shifts

## Slide 18: Shift Based Sample Generation
  Two types of Shift based collection
  Sample Interval
    Similar to Calendar time but only during a shift
    Allows for offsets at start and/or end of shift
  Samples Per Shift
  Both allow for sample expiry/warning
  Interval and Samples Per Shift can be combined

## Slide 19: Binary Attribute Characteristics
  Binary Attributes represent pass/fail data
  Measurement is taken and number of defectives are noted
  Variable sample sizes
    P charts
  Fixed sample sized
    Np charts

## Slide 20: Lab 7 Creating the Nut Quality Sample Plan
20 min

## Slide 21: Lab 8 Creating the Bag Quality Sample Plan
15 min

## Slide 22: Sample Recording Object
The Sample Recording Object (SRO) is
an ArchestrA automation object for
two-way communication between the
user and the Wonderware MES
database through the MES Middleware.

## Slide 23: Sample Recording Object
  The SRO configuration exposes the properties available for configuration and viewing

## Slide 24: Sample Recording Object
  Some of the properties of the SRO include
  Sample ID
    Specifies the ID (an integer) of the sample for which the data is to be recorded in the MES database
  Segment Requirement / Response
    Specifies the S95 segment requirement / response values for the sample
  Lot / Sublot
    Specifies the lot / sublot numbers for the sample.

## Slide 25: Sample Recording Object
  Some of the properties of the SRO include
  Operator
    Specifies the user/operator who pulls the sample from the production line or finalizes the sample
    No default connection to application Galaxy
  Final
    Specifies a boolean value that indicates whether the sample data is final
  Priority
    Specifies an integer value that identifies the priority for the sample.

## Slide 26: Sample Recording Object
  The Sample Viewer Control allows for basic data entry / editing
  Characteristic data
  Sample data
    Lot / Sublot
    Segment requirement / response
  Sample Pulling / Finalizing

## Slide 27: Sample Recording Object
  The Sample Viewer Control does not allow editing access to all SRO data, but all points are available for viewing and/or editing via the SRO

## Slide 28: Sample Recording Object
  A user interface can be created to allow for easy access to these properties

## Slide 29: Sample Recording Object
  As user interface for the most common SRO properties and features is available to for download from the Wonderware Developer Network
These tools have been made available as a part of this class

## Slide 30: Lab 9 Exploring the Additional Features of the SRO
35 min