## Slide 1: ABC analysis

## Slide 2: What is ABC analysis?
ABC analysis is an inventory categorization method which consists in dividing items into three categories (A, B, C):
  A being the most valuable items,
  C being the least valuable ones.
This method aims to draw managers’ attention on the critical few (A-items) not on the trivial many (C-items).

## Slide 3: The Pareto principle
VILFREDO PARETO (1848-1923)
  20% of population owns 80% of nations wealth
  20% of employees cause 80% of problems
  20% of items accounts for 80% of firms expenditure

## Slide 4: The ABC analysis
The ABC approach states that a company should rate items from A to C, basing its ratings on the following rules:
  A-items are goods which annual consumption value is the highest; the top 70-80% of the annual consumption value of the company typically accounts for only 10-20% of total inventory items.

## Slide 5: The ABC analysis
The ABC approach states that a company should rate items from A to C, basing its ratings on the following rules:
  B-items are the interclass items, with a medium consumption value; those 15-25% of annual consumption value typically accounts for 30% of total inventory items.

## Slide 6: The ABC analysis
The ABC approach states that a company should rate items from A to C, basing its ratings on the following rules:
  C-items are, on the contrary, items with the lowest consumption value; the lower 5% of the annual consumption value typically accounts for 50% of total inventory items.

## Slide 7: The ABC analysis

## Slide 8: The ABC analysis
The annual consumption value is calculated with the formula:
(Annual demand) x (item cost per unit)
Through this categorization, the supply manager can identify inventory hot spots, and separate them from the rest of the items, especially those that are numerous but not that profitable.

## Slide 9: The ABC analysis
Steps for the classification of items:
Find out the unit cost and and the usage of each material over a given period;
Multiply the unit cost by the estimated annual usage to obtain the net value;
List out all the items and arrange them in the descending value (Annual Value);

## Slide 10: The ABC analysis
Steps for the classification of items:
Accumulate value and add up number of items and calculate percentage on total inventory in value and in number;
Draw a curve of percentage items and percentage value;
Mark off from the curve the rational limits of A, B and C categories.

## Slide 11: ABC analysis
 | Percentage of items | Percentage value of annual usage | 
Class A items | About 20% | About 80% | Close day to day control
Class B items | About 30% | About 15% | Regular review
Class C items | About 50% | About 5% | Infrequent review

## Slide 12: Example 1
 | Percentage of items | Percentage value of annual usage | 
Class A items | About 20% | About 80% | Close day to day control
Class B items | About 30% | About 15% | Regular review
Class C items | About 50% | About 5% | Infrequent review

## Slide 13: Step 1
Calculate the total spending per year
Item number | Unit cost | Annual demand | Total cost per year
101 | 5 | 48,000 | 240,000
102 | 11 | 2,000 | 22,000
103 | 15 | 300 | 4,500
104 | 8 | 800 | 6,400
105 | 7 | 4,800 | 33,600
106 | 16 | 1,200 | 19,200
107 | 20 | 18,000 | 360,000
108 | 4 | 300 | 1,200
109 | 9 | 5,000 | 45,000
110 | 12 | 500 | 6,000
Total usage |  |  | 737,900
Total cost per year: Unit cost * total cost per year

## Slide 14: Step 2
Calculate the usage of item in total usage
Item number | Unit cost | Annual demand | Total cost per year | Usage as a % of total usage
101 | 5 | 48,000 | 240,000 | 32,5%
102 | 11 | 2,000 | 22,000 | 3%
103 | 15 | 300 | 4,500 | 0,6%
104 | 8 | 800 | 6,400 | 0,9%
105 | 7 | 4,800 | 33,600 | 4,6%
106 | 16 | 1,200 | 19,200 | 2,6%
107 | 20 | 18,000 | 360,000 | 48,8%
108 | 4 | 300 | 1,200 | 0,2%
109 | 9 | 5,000 | 45,000 | 6,1%
110 | 12 | 500 | 6,000 | 0,8%
Total usage |  |  | 737,900 | 100%
Usage as a % of total usage = usage of item/total usage

## Slide 15: Step 3
Sort the items by usage
Item number | Cumulative % of items | Unit cost | Annual demand | Total cost per year | Usage as a % of total usage | Cumulative % of total
107 | 10% | 20 | 18,000 | 360,000 | 48,8% | 48,8%
101 | 20% | 5 | 48,000 | 240,000 | 32,5% | 81,3%
109 | 30% | 9 | 5,000 | 45,000 | 6,1% | 87,4%
105 | 40% | 7 | 4,800 | 33,600 | 4,6% | 92%
102 | 50% | 11 | 2,000 | 22,000 | 3,0% | 94,9%
106 | 60% | 16 | 1,200 | 19,200 | 2,6% | 97,5%
104 | 70% | 8 | 800 | 6,400 | 0,9% | 98,4%
110 | 80% | 12 | 500 | 6,000 | 0,8% | 99,2%
103 | 90% | 15 | 300 | 4,500 | 0,6% | 99,8%
108 | 100% | 4 | 300 | 1,200 | 0,2% | 100%
Total usage |  |  |  | 737,900 | 100% | 

## Slide 16: Step 4
Results of calculation
Cathegory | Items | Percentage of items | Percentage usage (%) | Action
Class A | 107, 101 | 20% | 81,6% | Close control
Class B | 109, 105, 102, 106 | 40% | 16,2% | Regular review
Class C | 104, 110, 103, 108 | 40% | 2,5% | Infrequent review

## Slide 17: Additional rules for ABC analysis
Cathegory | Percentage of items | Percentage of usage
Class A items | 5-25% | 40-80%
Class B items | 20–40% | 15-40%
Class C items | 40-75% | 5-20%
A ≤ B ≤ C

## Slide 18: Inventory management policies
Each item should receive a treatment corresponding to its class:
  A-items should have tight inventory control, more secured storage areas and better sales forecasts; reorders should be frequent, with weekly or even daily reorder; avoiding stock-outs on A-items is a priority.

## Slide 19: Inventory management policies
Each item should receive a treatment corresponding to its class:
  B-items benefit from an intermediate status between A and C; an important aspect of class B is the monitoring of potential evolution toward class A or, in the contrary, toward the class C.

## Slide 20: Inventory management policies
Each item should receive a treatment corresponding to its class:
  Reordering C-items is made less frequently; a typically inventory policy for C-items consist of having only 1 unit on hand, and of reordering only when an actual purchase is made; this approach leads to stock-out situation after each purchase which can be an acceptable situation, as the C-items present both low demand and higher risk of excessive inventory costs.

## Slide 21: Procurement and Warehouse Applications
The results of an ABC Analysis extend into a number of other inventory control and management processes:
  Review of stocking levels: “A” items will generally have greater impact on projected investment and purchasing spend, and therefore should be managed more aggressively in terms of minimum and maximum inventory levels; inactive items will fall to the bottom of the prioritized list; the bottom of the “C” category is the best place to start when performing a periodic obsolescence review.

## Slide 22: Procurement and Warehouse Applications
The results of an ABC Analysis extend into a number of other inventory control and management processes:
  Cycle counting: the higher the usage, the more activity an item is likely to have; to ensure accurate record balances, higher priority items are cycle counted more frequently; “A” items are counted once every quarter; “B” items once every 6 months; and “C” items once every 12 months.

## Slide 23: Procurement and Warehouse Applications
The results of an ABC Analysis extend into a number of other inventory control and management processes:
  Identifying items for potential consignment or vendor stocking: since “A” items tend to have a greater impact on investment, these would be the best candidates to investigate the potential for alternative stocking arrangements that would reduce investment liability and associated carrying costs.

## Slide 24: Procurement and Warehouse Applications
The results of an ABC Analysis extend into a number of other inventory control and management processes:
  Turnover ratios and associated inventory goals: “A” items will have greater usage than “B” or “C” items, and as a result should have greater turnover ratios; when establishing investment and turnover metrics, inventory data can be segregated by ABC classification, with different targets for each category.

## Slide 25: Example 2
Item number | Annual quantity used | Unit value
1 | 75 | 80
2 | 150,000 | 0,9
3 | 500 | 3,0
4 | 18,000 | 0,20
5 | 3,000 | 0,30
6 | 20,000 | 0,10
7 | 10,000 | 2

## Slide 26: Step 1
Item number | Annual quantity used | Unit value | Usage per year
1 | 75 | 80 | 6,000
2 | 150,000 | 0,9 | 135,000
3 | 500 | 3,0 | 1,500
4 | 18,000 | 0,20 | 3,600
5 | 3,000 | 0,30 | 900
6 | 20,000 | 0,10 | 2,000
7 | 10,000 | 2 | 20,000
Total usage |  |  | 169,000

## Slide 27: Step 2
Item number | Annual quantity used | Unit value | Usage per year | Percentage in total usage (%)
1 | 75 | 80 | 6,000 | 3,51%
2 | 150,000 | 0,9 | 135,000 | 79,8%
3 | 500 | 3,0 | 1,500 | 0,87%
4 | 18,000 | 0,20 | 3,600 | 2,1%
5 | 3,000 | 0,30 | 900 | 0,53%
6 | 20,000 | 0,10 | 2,000 | 1,18%
7 | 10,000 | 2 | 20,000 | 11,8%
Total usage |  |  | 169,000 | 

## Slide 28: Step 3
Item number | Cumulative % of items | Annual quantity used | Unit value | Usage per year | Percentage in total usage (%) | Cumulative % of total
2 | 14% | 150,000 | 0,9 | 135,000 | 79,8% | 79,8%
7 | 29% | 10,000 | 2 | 20,000 | 11,8% | 91,6%
1 | 42% | 75 | 80 | 6,000 | 3,51% | 95,11%
4 | 56% | 18,000 | 0,20 | 3,600 | 2,1% | 97,21%
6 | 71% | 20,000 | 0,10 | 2,000 | 1,18% | 98,39%
3 | 84% | 500 | 3,0 | 1,500 | 0,87% | 99,46%
5 | 100% | 3,000 | 0,30 | 900 | 0,53% | 100%
Total usage |  |  |  | 169,000 |  | 

## Slide 29: Step 4
Cathegory | Items | Percentage of items | Percentage of usage (%) | Action
Class A items | 2 | 15% | 79,8% | Close control
Class B items | 7, 1 | 30% | 15,31% | Regular review
Class C items | 3, 4, 5, 6 | 55% | 4,89% | Infrequent review

## Slide 30: Conclusion
The boundary between class A and class B might not be as sharply defined;
The purpose of this classification is to ensure that purchasing staff use resources to maximum efficiency by concentrating on those items that have the greatest potential savings → selective control will be more effective than an approach that treats all items identically.