## Slide 1: Introduction to IT & Networking Basics

## Slide 2: Introduction of IT Activities
SSM is one of the leading organization in the field of Industrial Software, IT and Automation Solutions.
Out expertise in software process automation, industrial software, IT support and services.
Our achievements are 500+ Software Projects, 600+ Automation Projects and managing more than 3500 nodes of IT network.
We give highest preference to our customer and we try every best possible solution to keep our customer satisfied and happy.
We provide comprehensive IT Solutions like –
  FMS Support
  Network Management support
  System upgrade and maintenance
  Special contract for IT of Automation Systems like Servers of DCS and PLC
  IT Security service and support for firewall and DMZ configurations, CCTV, RFID, Access Control etc.

## Slide 3: Introduction of IT Activities
We also provide Software Solutions and Services like –
  Software upgrades, maintenance support and consulting
  Customized Software Development for IIOT, Mobile Platform, Web or specific solutions
  Software solutions development and consultancy services
IT Infrastructure and Networks at SSM Office –
  We have 50+ servers installed in our server room for different applications and team who all are working in office.
  We have defined different networks for different team for better network management and security purpose.

## Slide 4: Introduction of SSM Office IT Network Diagram

## Slide 5: Introduction of SSM Office Data Centre Diagram

## Slide 6: Introduction of Server Hardware Types and Operating System
What is Server Hardware – A server is a computer that provides data to other computers. While any computer can be configured as a server, most large businesses use rack-mountable hardware designed specifically for server functionality.
Servers are generally utilized to manage a network’s resources and provide services to the users in that network. The type of server hardware may depend on the dedicated service that server provides, as some hardware is better suited for certain purposes.
Types of Server Hardware – Tower Servers, Rack Servers, Blade Servers and Mainframes each provide different advantages.
Introduction to Server components like types of HDD, ISA and PCI Cards, UPS, Motherboard
Introduction of various ports on PC like Serial, Parallel, Ethernet, USB, VGA, HDMI, dvi etc.

## Slide 7: Introduction of Server Hardware Types and Operating System
Tower Servers –
  Tower servers are singular computers with the dedicated purpose of a server – they are housed in a standalone upright cabinet, or “tower”, much like the tower of a personal desktop computer.
  Towers provide their own unique advantages. Because of the low interior component density, they are easier to cool than rack or blade servers. The encased design allows room for more hardware or drive installation if necessary.
  Tower servers are much less space efficient. A set of tower servers will be much heavier and space-consuming than their thinner counterparts. Cable management can be complicated and bulky, and the air cooling from tower fans can be noisy.

## Slide 8: Introduction of Server Hardware Types and Operating System
Rack Servers –
  Just as the title implies, rack servers are designed to be mounted in a modular rack design for efficient management and storage.
  Rack servers are very versatile in their ability to manage different tasks and workloads, and they can maximize utility in one dedicated location.
  A major advantage to rack servers is the ease with which server components can be removed if necessary. Some businesses may desire a more modular design for ease of replacement – especially if that business is running a large operation with servers that may become defunct at different times.
  Because rack server bays are generally stacked tightly, efficient cooling can be a challenge. A dedicated cooling system is necessary to ensure no functionality is lost from overheating.

## Slide 9: Introduction of Server Hardware Types and Operating System
Blade Servers –
  Blade servers are chassis-based servers similar to rack servers, but the more stripped-down design allows for even more space efficiency than rack servers, among other key advantages.
  These server systems are comprised of individual server “blades”, thin dedicated server boards that each have individual processing power, memory capacity and a simple modular design that allows for easy configurability.
  Blade servers offer more processing power and ease of cable management than rack servers, but these advantages come with a larger price tag.

## Slide 10: Introduction of Server Hardware Types and Operating System
Mainframes –
  A mainframe is a large-scale computer with a sophisticated design and high workload capacity. Mainframes are large machines – about the size of a refrigerator or a stacked washer and dryer. They feature many swappable components, and are highly configurable.
  Mainframes are technically separated categorically from normal data center servers, as they generally run on their own unique operating systems and have a far larger performance capacity..
  Generally, mainframes are utilized by industries with high data volume and a necessity for reliable and secure computing. Mainframe servers are far more expensive than any other servers, but they are unrivaled in their resiliency and sheer computing power.

## Slide 11: Introduction of Server Hardware Types and Operating System
Server Operating System –
  A server operating system (OS) is a type of operating system that is designed to be installed and used on a server computer. It is an advanced version of an operating system, having features and capabilities required within a client-server architecture or similar enterprise computing environment.
Why is it necessary !
  Basically what Server OS does is – it provides an interface between the user and the system or application which can be graphical (Windows Server) or Terminal / Command Line (Unix or Linux etc.) based on the OS you are using.
  To help manage, store, send and process data large number of documents and their files.
  Flexible networking capabilities, Tight System Security, Transparent data transfer between different devices. Automation capabilities.
  Advanced backup facilities to permit regular and frequent online backups of critical data.
  Reconfigure and update both hardware and software to same extent.
Things to Look for in a Server OS
  Administration – what tools are available and how easy are they to use.
  Security – perhaps the most important feature and the hardest to judge and get right.

## Slide 12: Introduction of Server Hardware Types and Operating System
Things to Look for in a Server OS
  Stability – what is the downtime.
  Features – does it have the specific services you want built in for instance or an FTP server for remote file access.
  Performance – is the Server OS and the hardware platform is runs on fast enough for your needs.
  Scalability – how many clients can reasonably access this system.
  Third Party Application – what products are available for the platform.
  Hardware Requirements – whether the Server OS can run on Intel or AMD hardware or whether it requires a proprietary platform.
Most Common Server OS is Microsoft Windows Server OS
  Windows Server 2019
  Windows Server 2016
  Windows Server 2012 R2
  Windows Server 2012

## Slide 13: Introduction of Active Directory and Domain Policies
Active Directory
  Active Directory is a Directory Service which Contains Information of All User Accounts and Shared Recourses on a Network. Active Directory is a Centralized Hierarchical Directory Database ACTIVE DIRECTORY

## Slide 14: Introduction of Active Directory and Domain Policies
Active Directory
  Active Directory is a Directory Service which Contains Information of All User Accounts and Shared Recourses on a Network. Active Directory is a Centralized Hierarchical Directory Database ACTIVE DIRECTORY
Purpose of Active Directory
  Provide User Logon and Authentication Services
  To Organize and Manage – User Accounts, Computers, Groups and Network Resources
  Enables authorized users to easily locate – network resources
Features of Active Directory
  Fully Integrated Security
  Easy Administration using Group Policy
  Scalable to any Size Network
  Flexible
  Rename Computer Names and Domain Names
  Cross Forest Trust Relationship
  Site to Site Replication is faster

## Slide 15: Introduction of Active Directory and Domain Policies
Active Directory Diagram

## Slide 16: Introduction of Active Directory and Domain Policies
Domain Policy
  A domain security policy is a security policy that is specifically applied to a given domain or set of computers or drives in a given system. System administrators use a domain security policy to set security protocols for part of a network, including password protocols, access levels and much more.
  The primary purpose of Group Policy is to apply policy settings to computers and users in an Active Directory domain to enable IT administrators to automate one-to-many management of users and computers. This simplifies administrative tasks and reduces IT costs.
  An Active Directory environment means that you must have at least one server with the Active Directory Domain Services installed. Group Policy allows you to centralize the management of computers on your network without having to physically go to and configure each computer individually.

## Slide 17: Introduction of Application Layer Protocols
Application Layer Protocols
IP (Internet Protocol) –
  The Internet Protocol (IP) is the principal communications protocol in the Internet protocol suite for relaying datagrams across network boundaries. Its routing function enables internetworking, and essentially establishes the Internet.
  IP has the task of delivering packets from the source host to the destination host solely based on the IP addresses in the packet headers. For this purpose, IP defines packet structures that encapsulate the data to be delivered. It also defines addressing methods that are used to label the datagram with source and destination information.
TCP (Transmission Control Protocol) –
  The Transmission Control Protocol (TCP) is one of the main protocols of the Internet protocol suite. It originated in the initial network implementation in which it complemented the Internet Protocol (IP). Therefore, the entire suite is commonly referred to as TCP/IP. TCP provides reliable, ordered, and error-checked delivery of a stream of octets (bytes) between applications running on hosts communicating via an IP network. Major internet applications such as the World Wide Web, email, remote administration, and file transfer rely on TCP, which is part of the Transport Layer of the TCP/IP suite. SSL/TLS often runs on top of TCP.

## Slide 18: Introduction of Application Layer Protocols
Application Layer Protocols
DNS –
  DNS, Domain Name System Server is used to translate domain names to IP Addresses or used to translate IP Addresses to domain names.
  The idea is simple: to request server not by its IP-address (it's hard to remember for people), but by its normal name.

## Slide 19: Introduction of Application Layer Protocols
Application Layer Protocols
DHCP –
  DHCP, Dynamic Host Configuration Protocol Server is used to configure hosts mechanically / automatically.
  For DHCP to work, you need a DHCP-server, which will assign IP-addresses, and a DHCP-client on your device, which will request for an address. At home, the DHCP-server is usually located in router.

## Slide 20: Introduction of Application Layer Protocols
Application Layer Protocols
FTP (File Transfer Protocol) –
  It is one of the widely used application layer protocol of the TCP/IP protocol suite. FTP is basically used to exchange data between two host devices over the Internet or Intranet securely.
  It is referred to as one of the safest modes of file sharing among systems, and thus it is deployed by large industries, universities, and offices.
  It works in the client-server model and thus the user needs an FTP client program to run FTP on its system.
SMTP (Simple Mail Transfer Protocol) –
  SMTP is the standardization for transmission of electronic mails on the Internet. It is used by the e-mail server for sending and receiving messages, but the client host-based application only uses it for sending messages to the mail server. For receiving purposes, they use POP3 or IMAP.
  The outlook mail system of Microsoft system, Gmail and Yahoo mail, deploy SMTP for sending and retrieving emails from the exterior world whereas for interior mail exchange between their respective systems they use their own protocols.

## Slide 21: Introduction of Application Layer Protocols
Application Layer Protocols
POP (Post Office Protocol) –
  POP is also called as POP3 protocol.
  This is a protocol used by a mail server in conjunction with SMTP to receive and holds mails for host.
  POP3 mail server receives email and filters them into the appropriate user folder. When user connects to mail server to receive his emails, the messages are downloaded from mail server to local system.
HTTP (Hyper Text Transfer Protocol) –
  This protocol used mainly to access data on the World Wide Web (www).
  HTTP utilizes TCP connections to send client requests and server replies.
UDP (User Datagram Protocol) –
  UDP stands for User Datagram Protocol. It is a Transport Layer Protocol, which is a part of the Internet Protocol Suite and an alternative communication protocol to Transmission Control Protocol (TCP).

## Slide 22: Introduction of Application Layer Protocols
Application Layer Protocols
VPN Connection –
  A virtual private network (VPN) gives you online privacy and anonymity by creating a private network from a public internet connection. Most important, VPN services establish secure and encrypted connections to provide greater privacy than even a secured Wi-Fi hotspot.
  When you connect your computer (or another device, such as a smartphone or tablet) to a VPN, the computer acts as if it’s on the same local network as the VPN. All your network traffic is sent over a secure connection to the VPN. Because your computer behaves as if it’s on the network, this allows you to securely access local network resources even when you’re on the other side of the world. You’ll also be able to use the Internet as if you were present at the VPN’s location, which has some benefits if you’re using pubic Wi-Fi or want to access geo-blocked websites.
  Access a Business Network While Traveling:
  Access Your Home Network While Travelling:
  Hide Your Browsing Activity From Your Local Network and ISP:

## Slide 23: Introduction of Application Layer Protocols
Application Layer Protocols

## Slide 24: Introduction of IP Address Classes and Subnet Mask
Introduction of IP Address Classes and Subnet Mask (Sub netting) –
What is IP address?
  An IP address is a numeric identity of an interface. Just like a postal address provides a unique identity to a house, an IP address provides a unique identity to an interface.
Why an interface needs unique IP address?
  IP network uses IP address to find the destination interface and delivers the IP packets. In order to receive IP packets, an interface needs a unique IP address. If multiple interfaces have same IP address, IP network will not work.
How IP Address Works?
  IP address works in IP network just like a postal address works in postal system. A postal address is the combination of two addresses, area address and house address.
  Exact mechanism is used in IP network. An IP address is the combination of two addresses, network address and host address. Network address is the group address of all hosts which belong to a particular network and host address is the unique address of a specific host in that network.

## Slide 25: Introduction of IP Address Classes and Subnet Mask
IP Address Classes and Subnet Mask (Sub netting) –
IP address format
  An IP address is 32 bits in length. These bits are divided in four parts. Each part is known as octets and contains and 8 bits.
  An IP address can be written in dotted-decimal which is the most popular and frequently used method for writing an IP address.
  In dotted-decimal notation, each byte (8 bits) of the 32 bits IP address is written in decimal equivalent. The four resulting decimal numbers are separated by a dot and written in a sequence. 10.10.10.10, 172.168.10.1, 192.168.1.1 and 200.0.0.1 are some examples of IP address in dotted-decimal notation.
Subnet Mask
  Subnet mask is used to separate the network address from the host address in IP address.
  IP address is the combination of network address and host address, subnet mask helps us and programs which use IP address in identifying the network portion and the host portion.
  Just like IP address, subnet mask is also 32 bits in length and uses same notations which IP address uses to present itself.

## Slide 26: Introduction of IP Address Classes and Subnet Mask
IP Address Classes and Subnet Mask (Sub netting) –
IP address Classes
  There are 4,294,967,296 IP addresses. Managing all these addresses without any scheme are next to impossible. Let’s understand it with a simple example. If you have to find out a word from a language dictionary, how long will you take? Usually you will take less than five minutes to find out that word. You are able to do this because words in dictionary are organized in alphabetic order. If you have to find out the same word from the dictionary which does not use any sequence or order to organize the words, how long will you take this time? It may take up to one week to find out that specific word from all words.
  For easier management, IP addresses are organized in numeric order and divided in following five classes.

## Slide 27: Introduction of IP Routing and Forwarding
IP Routing –
  Routing and Switching are the basic functions of network communication.
  The function of Switching is to switch data packets between devices on the same network (or same LAN - Local Area Network).
  The function of Routing is to Route packets between different networks (between different LANs - Local Area Networks).
  IP Routing is the process of moving packets from one network to another network by using routers.
  What is Routing – When a router receives an IP packet, the router checks its routing table and compares all available paths to get the destination network of the received IP packet and selects the fastest path from all available paths. RIP, IGRP, EIGRP, and OSPF are examples of routing protocols.
  Why is Routing Important – It's vitally important to the Internet and we tend to overlook it until something goes wrong. Routing determines how packets (data sent over a network or networks) containing information, like email messages, website data, and voice-over-IP (VoIP) calls, move from one place to another on the Internet.

## Slide 28: Introduction of IP Routing and Forwarding
IP Routing –
  There are 3 types of routing:
    Static routing – Static routing is a process in which we have to manually add routes in routing table.
    Dynamic routing
    Default routing – This is the method where the router is configured to send all packets towards a single router (next hop).
  Static Routing –
    In static routing the routes are described by fixed path through a data network.
    The hosts which are present in the same router are entered by system administrator.
    No routing algorithm or update mechanisms are required.
  Dynamic Routing –
    Dynamic routing is used whenever the topology changes frequently.
    No need to entered the address belongs to the network manually.
    Here routing algorithms are used to calculate route to destination.

## Slide 29: Introduction of IP Routing and Forwarding
IP Routing –
  What is Routing Table – Routers use Routing Tables to determine out which interface the packet will be sent. A routing table lists all networks for which routes are known. Each router's routing table is unique and stored in the RAM of the device.
  Routing table is a data table stored in a router that lists the routes to particular network destinations, metrics (distances) associated with those routes.
  Each router/host has a routing table, indicating the path or the next hop for a given destination host or a network
  The router/host tries to match the destination
  address of a packet against entries in the
  routing table
  If there is a match, the router forwards it to the
  corresponding gateway router or directly to the
  destination host
  Default route is taken if no other entry matches
  the destination address

## Slide 30: Introduction of IP Routing and Forwarding
IP Routing –
IP Routing – finding the path
  Routing table entry (the path) is created by the administrator (static) or received from a routing protocol (dynamic)
  More than one routing protocol may run on a router – Each routing protocol builds its own routing table (Local RIB)
  Several alternative paths may exist – Best path selected for the router’s Global routing table (RIB)
  Decisions are updated periodically or as topology changes (event driven)
  Decisions are based on: – Topology, policies and metrics (hop count, filtering, delay, bandwidth, etc.)

## Slide 31: Introduction of IP Routing and Forwarding
Routing vs Forwarding –
  Routing = building maps and giving directions
  Forwarding = moving packets between interfaces according to the “directions”
IP Forwarding –
  Router decides which interface a packet is sent to
  Forwarding table populated by routing process
  Forwarding decisions –
    Destination address
    class of service (fair queuing, precedence, others)
    local requirements (packet filtering)

## Slide 32: Introduction of System Utilities
Everything –
  Everything is a desktop search utility for Windows that can rapidly find files and folders by name.

## Slide 33: Introduction of System Utilities
NetSetMan –
  NetSetMan is a network settings manager software which can easily switch between your preconfigured profiles like IP, Gateway, DNS, WINS - Multiple IPs per NIC - IPv4 & IPv6!
  You can change your workgroup on the fly!
  Expert setting: Only change the hardware address of a NIC if you really know what you're doing!

## Slide 34: Introduction of System Utilities
Registry Manager –
  Registry Manager is an advanced and complete suite of tools that allows you to safely maintain your local registry as well as the registries on the systems of your network.
  It provides security editors which allow you to set access permissions on your registry keys.

## Slide 35: Introduction of Networking Concepts
Data Transmission
  In modern networks, data are transferred using packet switching.
  Messages are broken into units called packets, and sent from one computer to the other.
  At the destination, data are extracted from one or more packets and used to reconstruct the original message.
  Each packet has a maximum size, and consists of a header and a data area.
  The header contains the addresses of the source and destination computers and sequencing information necessary to reassemble the message at the destination.

## Slide 36: Introduction of Basic Networking Concepts and Fundamentals
A network can be defined as a group of computers and other devices connected in some ways so as to be able to exchange data.
Essential components of the computer network – A computer network is built from the four essential components; End devices, Media, Protocols and Networking devices.
End Devices – like PC, Laptops, Desktops, Smart Terminals, Smart Phones etc.
Media – The media provides connectivity between the end devices. Unless end devices are connected through the any kind of media, they cannot exchange the data or service. Mainly there are two types of media; Wireless media and wired media.
  Wired – Coaxial, Twisted Pair, Fiber Optic i.e. UTP cables (Cat5 Cat6 cables), Serial cables, Fiber Optic cables.

## Slide 37: Introduction of Basic Networking Concepts and Fundamentals
Media –
  Types of Fiber Optic cable – There are three types of fiber optic cable commonly used: Single mode, Multimode and Plastic Optical Fiber (POF). Transparent glass or plastic fibers which allow light to be guided from one end to the other with minimal loss.

## Slide 38: Introduction of Basic Networking Concepts and Fundamentals
Media –
  Types of connectors
    Unshielded Twisted Pair (UTP) ...
    Shielded Twisted Pair (STP) ...
    Multi-Mode Fiber (MMF) ...
    Single Mode Fiber (SMF) ...
    Registered Jack 45 (RJ45) ...
    Straight Tip (ST) ...
    Subscriber Connector (SC) ...
    Lucent Connector (LC)

## Slide 39: Introduction of Basic Networking Concepts and Fundamentals
Media –
  Crimping of Ethernet Cable with Crimping Tool

## Slide 40: Introduction of Basic Networking Concepts and Fundamentals
Media –
  Cable tester for Ethernet cables.

## Slide 41: Introduction of Basic Networking Concept
Types of Networks
There are two principle kinds of networks:
  Wide Area Networks (WANs) and
  Local Area Networks (LANs).
WANs
  Cover cities, countries, and continents.
  Based on packet switching technology
  Examples of WAN technology: Asynchronous Transfer Mode (ATM), Integrated Services Digital Network (ISDN)
LANs
  Cover buildings or a set of closely related buildings.
  Examples of LAN technology: Ethernet, Token Ring, and Fibber Distributed Data Interconnect (FDDI).
  Ethernet LANs: based on a bus topology and broadcast communication
  Token ring LANs: based on ring topology
  FDDI LANs: use optical fibbers and an improved token ring mechanism based on two rings flowing in opposite directions.

## Slide 42: Introduction of Basic Networking Devices with Function
Network Interface Card (NIC)
  In the list of the networking devices, NIC stands on the first place. Without this device, networking cannot be done.
  This is also known as network adapter card, Ethernet Card and LAN card. NIC allows a networking device to communicate with the other networking device.
  NIC converts the data packets between two different data transmission technologies.
  A PC uses parallel data transmission technology to transmit the data between its internal parts while the media that provides connectivity between different PCs uses serial data transmission technology.

## Slide 43: Introduction of Basic Networking Devices with Function
Hub
  Hub is a centralized device that connects multiple devices in a single LAN network.
  Passive Hub: - It forwards data signals in the same format in which it receives them. It does not change the data signal in any manner.
  Active Hub: - It also works same as the passive Hub works. But before forwarding the data signals, it amplifies them. Due to this added feature, the active Hub is also known as the repeater.

## Slide 44: Introduction of Basic Networking Devices with Function
Bridge
  Bridges improve network throughput and operate at a more intelligent level than do hubs.
  A bridge is considered to be a store and forward device that uses unique hardware addresses to filter traffic that would otherwise travel from one segment to another.

## Slide 45: Introduction of Basic Networking Devices with Function
Switches
  Switches use bridging technology to forward traffic between ports. They provide full dedicated transmission rates between two stations that are directly connected to the switch ports.
  Replacing the two hubs and the bridge with an Ethernet switch provides the users with dedicated bandwidth. Each station has a full 10Mbps “pipe” to the switch. With a switch at the center of the network, combined with the 100Mbps links, users have greater access to the network.

## Slide 46: Introduction of Basic Networking Devices with Function
Routers
  A router has two basic functions, path determination using a variety of metrics, and forwarding packets from one network to another.
  Routing metrics can include load on the link between devices, delay, bandwidth, and reliability, or even hop count (i.e. the number of devices a packet must go through in order to reach its destination).
  In essence, routers will do all that bridges and switches will do, plus more. The router connects the different network segments. It switches the data packets between those networks which are either located in the different logical segments or built with the different network layer protocols.

## Slide 47: Introduction of Basic Networking Devices with Function
Wi-Fi Routers
  What is Wi-Fi Router and How Does it works? –
  A wireless router connects directly to a modem by a cable. This allows it to receive information from — and transmit information to — the internet. The router then creates and communicates with your home Wi-Fi network using built-in antennas. As a result, all of the devices on your home network have internet access.
  Wi-Fi routers are also used for NAT and Port Forwarding i.e. In computer networking, port forwarding or port mapping is an application of network address translation (NAT) that redirects a communication request from one address and port number combination to another while the packets are traversing a network gateway, such as a router or firewall.

## Slide 48: Introduction of Basic Networking Devices with Function
Router Basics –
  A router is a Network layer device, so it can work with the network packets at a higher level. In particular, a router can examine the IP address of the packets that pass through it. And because IP addresses have both a network and a host address, a router can determine what network a message is coming from and going to.
  The functional distinctions between bridges and routers — and switches and hubs, for that matter — get blurrier all the time. As bridges, hubs, and switches become more sophisticated, they’re able to take on some of the chores that used to require a router, thus putting many routers out of work.
  Some routers are nothing more than computers with several network interface cards and special software to perform the router functions.
  Routers can also connect networks that are geographically
  distant from each other via a phone line (using modems)
  or ISDN or Leased Lines.
  You can also use a router to join your LAN to the Internet.

## Slide 49: Introduction of Basic Networking Devices with Function
Firewall
  A firewall is a network security device that monitors incoming and outgoing network traffic and decides whether to allow or block specific traffic based on a defined set of security rules.
  Firewalls have been a first line of defense in network security for over 25 years.
  A firewall can be hardware, software, or both.

## Slide 50: Introduction of Basic Networking Devices with Function
Firewall Basics –
Hardware Firewall
  In this type of firewall, firewall is installed in a dedicated device. This device only runs the firewall. Since all resources of the device are available only for the firewall, it filters the traffic blazingly fast and accurate. It also offers several additional security features such as encryption and logging.
  Hardware firewalls are complex in configuration.
  Fast speed and max accuracy are the advantages of the hardware firewall while high cost and complex configuration are the disadvantages of this firewall.
Software Firewall
  In this type of firewall, firewall is installed in a regular device. This device runs the firewall as the application software. Since this firewall accesses device resources in shared environment through the base system, it provides less speed and accuracy than the hardware firewall. Unlike hardware firewall, it provides limited features and functions.
  Software firewalls are easier in configuration.
  Low cost and easier configuration are the advantages of the software firewall while slow speed, less accuracy and lack of additional features are the disadvantages of this firewall.

## Slide 51: Introduction of Basic Networking Devices with Function
Windows Firewall
  Windows Firewall is a Microsoft Windows application that filters information coming to your system from the Internet and blocking potentially harmful programs. The software blocks most programs from communicating through the firewall.
  The Windows Firewall is used to protect your Windows system from network-based threats. You can control who has access to your system and what access is granted. The Windows Firewall applet allows you to configure these firewall settings.
What is Firewall Policies and Rules?
  Firewall Rules examine the control information in individual packets. The Rules either block or allow those packets based on rules that are defined on these pages. Firewall Rules are assigned directly to computers or to policies that are in turn assigned to a computer or collection of computers.
What is Firewall Security Policies?
  A firewall policy defines how an organization's firewalls should handle inbound and outbound network traffic for specific IP addresses and address ranges, protocols, applications, and content types based on the organization's information security policies.

## Slide 52: Introduction of Basic Networking Devices with Function
What is Firewall Access Control list?
  Access Control Lists (ACLs) are a collection of permit and deny conditions, called rules, that provide security by blocking unauthorized users and allowing authorized users to access specific resources. ... Normally ACLs reside in a firewall router or in a router connecting two internal networks.
NAT and Port Forwarding
  What is NATing and Port Forwarding?
  NAT and port forwarding are different, but they are often used in conjunction with each other.
  NAT is network address translation. It translates traffic from one IP address to another.
  Port Forwarding (sometimes called PAT - Port Address Translation) is similar, but it functions on the port level.
  In computer networking, port forwarding or port mapping is an application of network address translation (NAT) that redirects a communication request from one address and port number combination to another while the packets are traversing a network gateway, such as a router or firewall.

## Slide 53: Introduction of Basic Networking Commands
Basic Networking Commands Explained with Examples
Ping –
  Verifies IP-level connectivity to another TCP/IP computer by sending Internet Control Message Protocol (ICMP) Echo Request messages. The receipt of corresponding Echo Reply messages are displayed, along with round-trip times. Ping is the primary TCP/IP command used to troubleshoot connectivity, reachability, and name resolution.
  You can use ping to test both the computer name and the IP address of the computer. If pinging the IP address is successful, but pinging the computer name is not, you might have a name resolution problem.

## Slide 54: Introduction of Basic Networking Commands
Basic Networking Commands Explained with Examples
Ping –
  Verifies IP-level connectivity to another TCP/IP computer by sending Internet Control Message Protocol (ICMP) Echo Request messages. The receipt of corresponding Echo Reply messages are displayed, along with round-trip times. Ping is the primary TCP/IP command used to troubleshoot connectivity, reachability, and name resolution.
  You can use ping to test both the computer name and the IP address of the computer. If pinging the IP address is successful, but pinging the computer name is not, you might have a name resolution problem.
  Syntax : Ping –t google.com
Tracert / traceroute
  This diagnostic tool Determines the path taken to a destination by sending Internet Control Message Protocol (ICMP) Echo Request messages to the destination with incrementally increasing Time to Live (TTL) field values.
  Examples:
  To trace the path to the host named www.google.co.in use following command
  tracert www.google.co.in

## Slide 55: Introduction of Basic Networking Commands
Basic Networking Commands Explained with Examples
Tracert / traceroute
  Syntax –
  tracert [-d] [-h MaximumHops] [-j HostList] [-w Timeout] [TargetName]

## Slide 56: Introduction of Basic Networking Commands
Basic Networking Commands Explained with Examples
Arp
  Displays and modifies entries in the Address Resolution Protocol (ARP) cache, which contains one or more tables that are used to store IP addresses and their resolved Ethernet or Token Ring physical addresses.
  Syntax –
  arp [-a [InetAddr] [-N IfaceAddr]] [-g [InetAddr] [-N IfaceAddr]] [-d InetAddr [IfaceAddr]] [-s InetAddr EtherAddr [IfaceAddr]]

## Slide 57: Introduction of Basic Networking Commands
Basic Networking Commands Explained with Examples
Netstat
  Displays active TCP connections, ports on which the computer is listening, Ethernet statistics, the IP routing table, IPv4 statistics (for the IP, ICMP, TCP, and UDP protocols), and IPv6 statistics (for the IPv6, ICMPv6, TCP over IPv6, and UDP over IPv6 protocols).
  Netstat provides statistics for the following:
  Proto - The name of the protocol (TCP or UDP).
  Local Address - The IP address of the local computer and the port number being used. The name of the local computer that corresponds to the IP address and the name of the port is shown unless the -n parameter is specified. If the port is not yet established, the port number is shown as an asterisk (*).
  Foreign Address - The IP address and port number of the remote computer to which the socket is connected. The names that corresponds to the IP address and the port are shown unless the -n parameter is specified. If the port is not yet established, the port number is shown as an asterisk (*).

## Slide 58: Introduction of Basic Networking Commands
Basic Networking Commands Explained with Examples
Netstat
  (state) Indicates the state of a TCP connection. The possible states are as follows:
  CLOSE_WAIT
  CLOSED
  ESTABLISHED
  FIN_WAIT_1
  FIN_WAIT_2
  LAST_ACK
  LISTEN
  SYN_RECEIVED
  SYN_SEND
  TIMED_WAIT
  Syntax : netstat [-a] [-e] [-n] [-o] [-p Protocol] [-r] [-s] [Interval]

## Slide 59: Introduction of Basic Networking Commands
Basic Networking Commands Explained with Examples
Nbtstat
  Displays NetBIOS over TCP/IP (NetBT) protocol statistics
  NetBIOS name tables for both the local computer and remote computers, and the NetBIOS name cache. Nbtstat allows a refresh of the NetBIOS name cache and the names registered with Windows Internet Name Service (WINS).
  Syntax : nbtstat [-a RemoteName] [-A IPAddress] [-c] [-n] [-r] [-R] [-RR] [-s] [-S] [Interval]

## Slide 60: Introduction of Basic Networking Commands
Basic Networking Commands Explained with Examples
Ipconfig
  Displays all current TCP/IP network configuration values and refreshes Dynamic Host Configuration Protocol (DHCP) and Domain Name System (DNS) settings.
  This command is most useful on computers that are configured to obtain an IP address automatically.
  This enables users to determine which TCP/IP configuration values have been configured by DHCP, Automatic Private IP Addressing (APIPA), or an alternate configuration.
  Syntax : ipconfig [/all] [/renew [Adapter]] [/release [Adapter]] [/flushdns] [/displaydns] [/registerdns] [/showclassid Adapter] [/setclassid Adapter [ClassID]]

## Slide 61: Introduction of Basic Networking Commands
Basic Networking Tools
IP Scanner
  IP Scanner is a tool that is quite useful in the field of networking. The IP Scanner is, as its name indicates, a scanner that scans for IP addresses and various other information of the devices on your network. So, in short, the IP scanner scans your network for devices and information relevant to them.

## Slide 62: Introduction of Basic Networking Commands
Basic Networking Tools
Wireshark
  Wireshark is the world’s foremost and widely-used network protocol analyzer. It lets you see what’s happening on your network at a microscopic level.
  Wireshark is a packet sniffer and analysis tool. It captures network traffic on the local network and stores that data for offline analysis. Wireshark captures network traffic from Ethernet, Bluetooth, Wireless (IEEE.802.11), Token Ring, Frame Relay connections, and more.

## Slide 63: Thank You